Embedded FPGA Control for Wireless Sensory Networks

Intelligent Embedded Systems - COM912
School of Computing and Intelligent Systems

1. Abstract
In today’s pervasive world, there is an ever growing interest to deploy sensors for monitoring various infrastructure systems for the purpose of condition monitoring, operational control, and security. Acquisition and analysis of this sensor information is important, as many intelligent systems use this data to examine the environment in which it is placed and respond with appropriate control strategies. Energy consumption and conservation is also critical in applications which are largely dependant on battery power. Many of the bandwidth and energy conservation issues can be alleviated by embedding processing capabilities within the sensor network. In this paper an FPGA based system is introduced to adequately solve the processing demands placed on today’s wireless sensory networks. A hybrid Hardware/Software design strategy is outlined. An example wireless sensory network to monitor temperature sensors is used as a relevant control application and to demonstrate the advantage of pre-processing sensory data and how this could be used to develop responding control strategies is discussed.

2. Introduction
Sensor Networks have evolved from traditional hard-wired systems to more intricate wireless networks with ever increasing functionality. This increased functionality has led to bigger demands on signal processing. Intelligent embedded systems can take advantage of greater processing power and flexibility to pre-process sensory information before transmission, and implement intelligent control strategies to monitored systems.

2.1 Wireless sensory Network applications
Many different applications for Wireless Sensory networks are being developed today, from Wireless Intelligent Sensors in the fabric of buildings to aid Structural Health Monitoring [1] to Sensor Networks in Agriculture Production [2] to monitor soil conditions and early alerts for frost damage. Condition Based Monitoring systems to replace manual fault monitoring techniques is another application area currently being developed. Also area monitoring for building security and military applications is of significant interest for wireless sensory networks. One of the main drawbacks of wireless sensor networks is that moving data consumes energy and other resources, including bandwidth. Various techniques have been researched to improve energy conservation in sensor network applications [3]. Employing Intelligent Embedded systems at sensor nodes within a sensor network is one approach [4, 5, 6]. For example, to measure the average temperature in a room, sensors could be continuously transmit data, and have a client application compute the average. In this particular case, there is no need for data to be continually streaming across the network. A more efficient approach is to embed local processing capabilities within the network sensor nodes. Therefore each network node can calculate an average temperature reading reported by the individual sensor, and send that figure back periodically, reducing the amount of data that must traverse the network. This Temperature monitoring and control example forms the basis of this papers design application.

3. Project Application
The Project centres around the implementation of a FPGA based micro-controller system which communicates with the wireless sensory network via the transceivers available on the i-Bean 5324 ZigBee ready Networking System from Millennial Net. The technology available and design tasks necessary to undertake this project are outlined in the following sections

3.1 Millennial Net iB-5324 Networking System
The iB-5324 Endpoint reduced function device (RFD) is a tiny microcomputer with analog and digital interfaces and a wireless communications link. It incorporates a UART Interface which permits communication with the microcontroller, an Analog to Digital converter used to obtain heat information from the temperature sensors. It also contains a MCU to control the UART, A/D and wireless communications to additional i-Bean Routers or Gateways.

3.2 Picoblaze 8-bit Microcontroller for Virtex-II series devices
The Picoblaze module is a fully embedded 8-bit microcontroller macro for the Xilinx Virtex-II series [7]. Its suitability to non-time critical processing of data makes the Picoblaze Microcontroller appropriate for this particular application. The Picoblaze module is totally embedded into the Virtex-II device and requires no external support. Any logic can be connected to the module inside the Virtex-II device, meaning that any additional features can be added to provide ultimate flexibility. The Picoblaze Microcontroller supports 16 byte wide General purpose data registers, 1K instructions of programmable on-chip memory store which is automatically loaded during FPGA configuration [8].

3.3 Design Tasks
The remit of this paper is to successfully implement the following design stages.
- Interfacing the Picoblaze Microcontroller with the UART
- Setting up the communications link between the FPGA and transceiver UART.
- Creating a software program for the microcontroller to interrupt and service the UART when data has been received.
- Processing the data by averaging the temperature over defined periods and returning the information to the Millennial Net gateway server

Figure 3.3 illustrates the high level system design, with the core of design being the embedded FPGA implementation.

Figure 3.3: Wireless Sensor Network Architecture

4. Embedded FPGA Design
From an early stage it became apparent that the FPGA design could be targeted at the XC2V40 Virtex-II device, eliminating the need to use the larger XC2V1000 device as originally outlined. This would realise significant savings in terms of cost and device utilisation. Furthermore, without the aid of a functional Millennial Net wireless sensor network to test the FPGA design, an alternative testing mechanism would be required. This implementation will be discussed later in the paper. The core design work of the paper can be broken up into three distinct stages, VHDL based Hardware Design, Software Programming of the Microcontroller and Testing strategy.

4.1 VHDL based Hardware design
The Xilinx Virtex-II implementation of the FPGA system involved connecting together the already available IP cores by instantiating the Picoblaze Microcontroller, Program ROM, UART RX and TX macros [9]. To simplify the top-level design, an embedded VHDL module is utilised in which the Picoblaze microcontroller is connected to its associated block RAM program ROM, reducing the need for two component declarations and instantiations. Likewise, both the UART receive and UART transmit modules are combined to form a single UART_TX_RX module. A simple Address decoder is used in the hardware design to differentiate between the UART receive status buffer and the receive data buffer. A Digital Clock Manager is also implemented to take advantage of certain features of this module, such as clock de-skew and flexible clock multiplication and division. To begin synthesis of the hardware components, a User Constraints File is created detailing the specific IO pin information targeted at the XC2V40 device and development board for testing at a later stage. Before the hardware design can be tested, a VHDL representation of the Program ROM is required. This module is automatically created by the KCPSM assembler. The assemblers reads the Picoblaze program source (.psm) and three template files that instantiate and initialize a block RAM in various design flows.
A simple source code program to load a value to a register is sufficient to assemble the.psm file, and generate the Program ROM VHDL file to be used for Logic Synthesis and simulation. By following through the various implementation stages within Xilinx ISE development environment, the hardware design can be checked for any errors during synthesis, and ensure the design will map, place and route to the relevant hardware.

4.2 Software Programming
The Picoblaze program ROM will have to contain a valid set of instructions to implement the software tasks outlined in section 3.3 of this paper. This will require a valid interrupt routine to successfully service the UART when data has been received via the Rx port. The software design will have to make efficient use of the scratchpad memory to store temperature information over a defined period, and utilise the Picoblaze instruction set to calculate an average temperature value. This average value will be transmitted via the UART Tx port.

4.3 Design Test strategy
The scope of this paper is an embedded FPGA control application for Wireless Sensory Networks. Without access to the appropriate Wireless Sensor Network, a suitable test strategy was required to emulate this network. As outlined in the Software Programming design phase, the application must interrupt and service the UART when data is received. This sensor data must then be processed by averaging temperature over hourly periods and returning the processed data via the UART to the gateway server. The paper outlines one such emulation approach, which involves two Virtex-II development boards. One board will imitate the Sensor network by transmitting data to UART. This data will be read and processed by the FPGA system. As both host and target applications are Picoblaze Microcontroller to UART transmission paths, the same hardware design can be used in both instances. With the sensor network emulation board having an associated program file to continuously transmit data to the UART.

5. Evaluation and Results
The Design and test strategy outlined in section 4 of this paper yielded the following results. The VHDL base Hardware Platform was successfully implemented. The design top level source code is shown in Appendix A. This illustrates the declaration and instantiation of the various component modules used in the design. Using the Xilinx Integrated Software Environment (ISE) the Hardware design was synthesised, mapped, placed and routed on its target device the XC2V40 Virtex-II. Table 5.1 demonstrates the XC2V40 device utilisation summary post synthesis. It should be noted at this point that this synthesis report does not include a complete Program ROM module, which will employ additional device resources.

Device utilization summary:

---------------------------

Selected Device : 2v40fg256-6

 Number of Slices: 162 out of 256 63%
 Number of Slice Flip Flops: 119 out of 512 23%
 Number of 4 input LUTs: 237 out of 512 46%
 Number of bonded IOBs: 5 out of 88 5%
 Number of BRAMs: 1 out of 4 25%
 Number of GCLKs: 2 out of 16 12%
 Number of DCM_ADVs: 1 out of 4 25%

Table 5.1: Post Synthesis Device utilisation summary

The next stage in the designs evaluation involved simulating the Hardware module to validate its functionality. Using the Modelsim simulation environment the paper can verify the functional correctness of the hardware design. By compiling a simple Program ROM file, various functions can be demonstrated in the simulation environment. Table 5.2 illustrates a sample of an Assembler source file to perform the following tasks:
- Load 2 internal data registers with constant values
- Write the register values to UART TX Register
- Read the Receive Status buffer of the UART

;-- 80h UART rx register

;-- 81h UART rx status buffer

load s07, 09
load s1C, 04

repeat:	output s1C, 00 ;-- write byte to UART tx register
output s07, 00 ;-- write byte to UART tx register
input s01, 81 ;-- read the receive status buffer of UART
jump repeat

Table 5.2: Picoblaze assembler source file

The simulation of this sample program can be seen in Figure 5.1. The diagram clearly shows both the loading of data into internal registers, and writing the contents of said registers to the UART Tx buffer. The simulation illustrates an attempted read of the UART Rx status buffer, however as there is nothing connected to the Rx port, a valid data read is not possible in this simulation.

Figure 5.1: Simulation Results

Post simulation, the next stage in evaluating the design involved the implementation of the system emulation, outlined in section 4.3 of this paper. This involved interconnecting two Xilinx XC2V40 Virtex-II development boards, one to act as the embedded FPGA control system and one to mimic the Sensory network UART Interface. This hardware emulation was configured, and a simple test program employed on the Sensory network board to keep the UART Tx Buffer full of temperature data. The project had difficulty in executing an adequate interrupt service routine on the FPGA control system, which subsequently resulted in a non functioning Hardware system to adequately represent the design. Beyond this paper, further investigation will be undertaken to successfully implement the design strategy previously outlined.

6. Conclusion
Although a working hardware implementation was not achieved, a functional Hardware platform and adequate test strategy have been put in place. Minor modifications to the Program ROM Instruction code are required to deliver on the project specification. The paper has outlined some of the possible applications for wireless sensory networks, and why such networks are evolving with localised processing of information, to alleviate bandwidth problems and assist energy conservation in a mobile technology environment. Further work could be undertaken to target such applications at other technologies which have sufficient processing capabilities and require less power, such as CPLD technology.

References
[1]	Sazonov, E; Janoyan, K; Jha, R, “Wireless Intelligent Sensor Network for Autonomous Structural Health Monitoring” Proceedings of SPIE: Smart Structures and Materials 2004; Smart Sensor Technology and Measurement Systems. Vol. SPIE Volume 5384, pp. 305-314. 2004
[2]	R. Beckwith, D. Teibel, and P. Bowen, “Pervasive Computing and Proactive Agriculture.” In Adjunct Proc. PERVASIVE 2004, Vienna, Austria, April 2004.
[3]	W.S. Conner, J. Chhabra, M. Yarvis, and L. Krishnamurthy, “Experimental Evaluation of Synchronization and Topology Control for In-Building Sensor Network Applications”, WSNA'03, September 2003
[4]	G.J. Pottie, W.J. Kaiser “Wireless Integrated Network Sensors”. Communications of the ACM, vol. 43, no. 5, pp. 551-8, May 2000.
[5]	Henry O. Marcy, Jonathan R. Agre, Charles Chien,Loren P. Clare, Nikolai Romanov, and Allen Twarowski, “ Wireless sensor networks for area monitoring and integrated vehicle health management applications”, AIAA Guidance, Navigation, and Control Conference and Exhibit, Portland, OR, Aug. 9-11, 1999, Collection of Technical Papers. Vol. 1 (A99-36576 09-63)
[6]	Gregory J. Pottie and Loren P. Clare, “Wireless integrated network sensors: toward low-cost and robust self-organizing security networks”, Proc. SPIE, Sensors, C3I, Vol. 3577, p. 86-95
[7]	Xilinx Picoblaze 8-Bit Microcontroller for Virtex-II Devices (V1.1) 2003
[8]	Picoblaze 8-Bit Microcontroller User Guide (V1.1) 2004
[9]	Xilinx UART Transceiver and Receiver Macros Oct 2002